## Slide 1: IN. SS-1: Accuracy of Estimates
Help one another but each person make own estimates and measurements.
May do Parts A, B, C, D & E in any order.
Do NOT open the “UNKNOWN”.
Do NOT remove top of distilled H2O bottle. Pour water into small beaker first then measure in graduated cylinder. Do NOT put unused H2O back into bottle. Dump in waste beaker.
Weigh 3 times. Record the average.
READ PART C STEP 9 CAREFULLY. Calculations are different.

## Slide 2: Reading Graduated Cylinder

## Slide 3: Care of the Balance
Do not move the balance.
Weigh in a cup – do not put anything directly on the balance.
Do not force the knob or dial. If it resists, stop turning!

## Slide 4: Directions for weighing:
Before weighing each item, zero the balance.
  - Set sliders and Vernier at zero.
  - Turn adjust knob until pointer is at zero.
Move slider weight to right one notch at a time until pointer drops.
Back up slider one notch.
Turn dial on vernier until arm points exactly at the zero line.

## Slide 5: Reading the Vernier
1. First number on dial to right of 0 line is the whole grams.
2. Count whole spaces on dial between 0 and that number. That is tells you the tenths of a gram.
3. On the Vernier (back plate) go left from the 0 until you get to the first line that aligns perfectly with a line on the dial. Count spaces between it and 0 on the Vernier (not on the dial). That is the hundredths of a gram.
3
.2
3
TO FIND THE TOTAL WEIGHT: Add this to whatever shows on the sliders. For example, if it is 60g:
60g
+3.23g
63.23g

## Slide 6: Practice
1. First number on dial to right of 0 line is the whole grams.
2. Count whole spaces on dial between 0 and that number. That is the tenths of a gram.
3. On the Vernier (back plate) go left from the 0 until you get to the first line that aligns perfectly with a line on the dial. Count spaces between it and 0 on the Vernier (not on the dial). That is the hundredths of a gram.
7.38

## Slide 7
4.46
Practice

## Slide 8: What if you want to know the weight of the water in this beaker?
Weigh beaker
Weigh beaker with water in it.
Subtract weight of beaker = weight of water.

## Slide 9: IN. SS-1: Accuracy of Estimates
Help one another but each person make own estimates and measurements.
May do Parts A, B, C, D & E in any order.
Do NOT open the “UNKNOWN”.
Do NOT remove top of distilled H2O bottle. Pour water into small beaker first then measure in graduated cylinder. Do NOT put unused H2O back into bottle. Dump in waste beaker.
Weigh 3 times!!! Record the average.
READ PART C STEP 9 CAREFULLY. Calculations are different.

## Slide 10: General Clean-up Requirements
Clean up all trash from trays, table, floor around and under table.
Leave all items in correct trays, as you found them.
Empty waste beaker if there is one.
Replace paper towel in tray if it is wet or dirty.
Leave table top clean AND dry.
Wash test tubes and leave upside down in rack so they will drain.
Rinse graduated cylinders and leave lying down on their sides in tray.
EVERYONE HELPS WITH CLEAN UP. No one leaves the table until it is clean. Assigned person notify teacher when table is clean. After teacher checks, assigned person sign out table.
LEAVE EVERYTHING AS YOU FOUND IT
– OR BETTER!!

## Slide 11: IN. SS-1: Accuracy of Estimates - Day 2
To avoid waiting for the balance, one pair start with Part D (WEIGHT), the other pair start with a different part.
Do NOT open the “UNKNOWN”.
Do NOT remove top of distilled H2O bottle.
Dump all extra or used liquids into WASTE beaker. Empty beaker at end of period.
READ PART C STEP 9 VERY CAREFULLY. Calculations are different.
After determining your average % accuracy, write your student # on the board in the corresponding category.
When you finish the procedures begin setting up your graph following the directions on the reference sheet.

## Slide 12
% Accuracy | TOTAL # students
100-96 | 2
95-91 | 1
90-86 | 2
85-81 | 9
80-76 | 4
75-71 | 18
70-66 | 13
65-61 | 8
60-56 | 4
55-51 | 8
% Accuracy | TOTAL # students
50-46 | 5
45-41 | 2
40-36 | 1
35-31 | 
30-26 | 
25-21 | 
20-16 | 
15-11 | 
10-6 | 1
5-0 | 
This is the data you will graph.
Data points always go on Y axis.
The scale that is fixed goes on the X axis.
DQ #1

## Slide 13
Relationship between attendance and grades.
Proper graphs of data:
Have a title.
Have labeled axes with units shown.
Have uniform increments on each axis.
Have a “Line of Best Fit” or trend line (not “connecting the dots”).
Overall grade in %
REQUIREMENTS for
GRAPHS:
On graph paper
In pencil
Use a ruler
(No carbon copy)
% of days attended

## Slide 14
A best-fit line reveals the underlying pattern or trend of data. Comes as close as possible to data points while smoothing out the “zigs and zags”. May or may not go through some or all data points.
What is the pattern? In other words, what is the relationship?
Relationship between Mass of Car and Distance required to Stop.

## Slide 15: “Best Fit” lines aren’t always straight.
Personal strength at different ages
What is the pattern?

## Slide 16: TO COMPLETE THIS WRITE-UP:
Do discussion questions. (1 is the class data table, 2 is the graph - so all you have left to do are #3 and 4.)
Write a conclusion:
  Follow Ref. Sheet 3 directions but write in paragraph form - DO NOT write a list. This is a very simple lab so your conclusion will probably only be a couple of paragraphs.
  Support your claims with data. Explain HOW the data supports your claim.
  DON’T STRESS OUT ABOUT THIS!! YOU’RE BASICALLY JUST TELLING WHAT HAPPENED IN THE LAB AND WHETHER OR NOT IT TURNED OUT THE WAY YOU PREDICTED.
  DO THE BEST YOU CAN. THE ONLY WAY TO LOSE IS BY NOT DOING IT!
  UPDATE: No conclusion required (for this lab only!).

## Slide 17
Example of graph of SS-1 data properly done.
NOTE: this includes all 4 classes. Periods 1-3, you did not have this much data (and that is perfectly fine!).